## Slide 1: A Program for Elsie, a 4-bit Computer
Or, Your Code Really Looks Like This

## Slide 2: What is a computer program?

## Slide 3: What is a computer program?
It’s a set of computer instructions that accomplish a task

## Slide 4: What is Elsie?

## Slide 5: Elsie is a tiny computer with a 4-bit bus

## Slide 6: Elsie can: Move a number from memory into Register A (where math can happen)

## Slide 7: Elsie can: Move a number from memory into the A register (where math can happen) Add a number to Register A

## Slide 8: Elsie can: Move a number from memory into the A register (where math can happen) Add a number to the A register Move the result back into memory

## Slide 9: Elsie, like all digital computers, only understands ones and zeros

## Slide 10: Elsie is really, really simple but

## Slide 11: All our computers work very much like Elsie

## Slide 12: So writing a program for Elsie shows us what programs really look like and how they run.

## Slide 13: What does a program for Elsie look like?

## Slide 14: # this is a line comment # (first thing’s first!)

## Slide 15: # these are the only instructions # Elsie knows load # move data value into regA add # add data value to regA store # store contents of regA goto # this one we skip for now

## Slide 16: # this program adds 1 + 2 and # stores the result in # memory location 10 load 1 add 2 sto 10

## Slide 17: How does Elsie know what to do?

## Slide 18: When Elsie powers up, the hardware starts reading 4 binary bits (a nybble) at a time.

## Slide 19: Where do these nybbles come from?

## Slide 20: Elsie has an Instruction Pointer, a register that knows where the next instruction is.

## Slide 21: Let’s have a look at Elsie

## Slide 23: Back to the 4-bit nybbles Elsie’s been reading all this time

## Slide 24: Elsie’s hardware endlessly feeds the CPU 4-bit nybbles in pairs

## Slide 25: The first nybble is the instruction. The second nybble is data for that instruction to use.

## Slide 26: Elsie’s hardware fetches a 4-bit instruction nybble,

## Slide 27: Elsie’s hardware fetches a 4-bit instruction nybble, fetches a 4-bit data nybble,

## Slide 28: Elsie’s hardware fetches a 4-bit instruction nybble, fetches a 4-bit data nybble, executes the instruction using the data, and

## Slide 29: Elsie’s hardware fetches a 4-bit opcode nybble, fetches a 4-bit data nybble, executes the instruction using the data, and repeats as long as power is on.

## Slide 30: On Elsie, each instruction has a 2-bit ID called an opcode: load = 00 add = 01 sto = 10 goto = 11

## Slide 31: Each 4-bit instruction nybble also contains a 2-bit mode that we skip for now
opcode | mode (always 00 for now)

## Slide 32: Back to our program..

## Slide 33: # this program adds 1 + 2 and # stores the result in # memory location 10 load 1 add 2 sto 10

## Slide 34: # this program is # much easier to read # with line comments! load 1 # put a 1 in register A add 2 # add 2 to register A sto 10 # store the result

## Slide 35: But Elsie only knows ones and zeros so we must translate

## Slide 36: We know the 2-bit opcode for each instruction, and

## Slide 37: We know the data for each instruction.

## Slide 38: To Elsie, our program looks like this load 1 0000 0001 add 2 0100 0010 sto 10 1000 1010

## Slide 39: (This translation to ones and zeros is what compilers do.)

## Slide 40: Elsie’s CPU is wired to execute each instruction.

## Slide 44: What do real computer instructions look like?

## Slide 45: A similar program in C++:

## Slide 46: Now the real computer instructions:

## Slide 47: Not too different from Elsie’s code, eh? load 1 0000 0001 add 2 0100 0010 sto 10 1000 1010